CITY OF PITTSBURGH

DEPARTMENT OF PUBLIC WORKS / DEPARTMENT OF MOBILITY AND INFRASTRUCTURE

DOWNTOWN TRAFFIC MODELING

REQUEST FOR PROPOSALS

The City of Pittsburgh is interested in building a complete model of transportation in the downtown area. Following the collection of traffic counts at all 75 intersections in the Central Business Districts, the city is requesting proposals for the completion of a downtown traffic model using these traffic counts.

As the first step in carrying out this priority, the City is requesting proposals for traffic counts in the Central Business District (CBD). There are 75 traffic signals in the CBD.

The City seeks proposals that (1) identifies specific staff and sub-consultants that are qualified and available to assist in any or all of the tasks outlined below (2) propose a schedule that can meet the deadlines outlined below.

## TASK 1 Build downtown transportation model

Using the traffic counts from the 75 downtown intersections, existing timing plans and building off of the existing VISSIM model created through the BRT project, build a complete dynamic model of Pittsburgh's downtown transportation system. The model should be capable of simulating, testing and reporting the systematic effect of new street geometries, lane configurations and signaling. It should take into account the interactions between motorized private vehicles, public transit, freight movement, pedestrians and bicyclists.

Right: Snapshot of exiting VISSIM model created through the BRT project

## TASK 2 Model and study bus Loop reversal

Model the effects of reversing the bus lanes on both Smithfield and Wood streets. New bus lanes should follow in the following configuration:

Smithfield street from Ft Pitt Boulevard to Liberty Avenue

One northbound bus lane One southbound travel lane One southbound peak hour travel lane (off-peak parking)

Wood street from Ft Pitt Boulevard to Liberty Avenue

One northbound peak hour travel lane (off-peak parking) One northbound travel lane One southbound bus lane

## TASK 3 Model and study the addition of bike lanes

Model the effects of adding bike lanes on Smithfield and Wood Street. New lanes should follow in the following configuration:

Smithfield street from Ft Pitt Boulevard to Liberty Avenue

One northbound bus lane One southbound travel lane One southbound bike lane One parking lane

Wood street from Ft Pitt Boulevard to Liberty Avenue

One parking lane One northbound bike lane One northbound travel lane One southbound bus lane

## TASK 4 Model up to 3 new operations plans

Use the newly created transportation model to study and test proposed operations plans that are slated for immediate implementation. Options include:

Option 1:

Turn the S Loop (minus 39, 40, 44) at Forbes Avenue

P1 along Liberty, L at Wood, L at 6th, L on Smithfield (in new buslane)

Option 2:

Turn the S Loop (minus 39, 40, 44) at Forbes

Take the P1 all the way to Gateway Islands turn arounds

Option 3:

Turn the S Loop (minus 39, 40, 44) at Forbes

Through-route the P1s to the West Busway

## TASK 5 Optimize downtown traffic signals

Prepare new operations plan that improves pedestrian and bicycle safety, optimizes and directs vehicular traffic towards chosen routes and optimizes bus operations along transit priority streets.

***need to decide what optimization means - e.g. is it clearing traffic or is it serving bus progression or making sure pedestrians don't have to wait long -- each may well result in a very different outcome)

## TASK 6 Prepare signal timing plans

Based on Task 5, prepare new signal timing plans for any changes proposed and accepted in the optimization process.

## WORK PRODUCTS

- Traffic model including all 75 downtown intersections

- Training to city employees on the use of the traffic model

- Reports outlining the effects of tasks 2-4

- Reports outlining the methods and effect of the optimized signals

- Prepare new signal timing plans for necessary intersections

## SCHEDULE

The schedule for Task 1 and 2 are condensed to meet the Port Authority's spring pick date of _______. If this level of effort is found to be unattainable in the timeframe provided, you may provide a proposal for the amount of work that can be completed in this timeframe. Please note any time savings that can be provided.

December 1, 2017, proposals due

December 15, 2017, notice to proceed

March 9, 2017, completion of tasks 1-4 (what is the PAAC's drop dead date for decisions RE:  spring pick?

June 2017, completion of tasks 5 and 6

Submit team resumes, description of project approach, and price proposal to kristin.saunders@pittsburghpa.gov by Friday, December 1, 2017 at 3:00 PM. Proposals should be emailed directly or with an FTP link. The subject line should read DOWNTOWN TRAFFIC MODELING.

A pre-submission meeting will not be held due to the short time frame requested, but if there are any questions please reply all on this email. All questions will be answered as quickly as possible.

signalized