City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME:

- What was the previous permitted use for this property?

The property is owned by Affirmative Investments, Inc. and located along Forbes Avenue. The site currently consists partially of gravel pavement, landscaping, and woodlands, but primarily of meadow conditions.

- What is the proposed use for the property?

The proposed use of the property is a new six-story multifamily housing building and associated landscaping and stormwater management.

- How is green stormwater mitigation being integrated into the proposed project?

Green stormwater mitigation is being integrated into the proposed project through the use of a Managed Release Concept rate and volume control system. Stormwater is collected from pavements, roof drains, and outdoor recreation areas and conveyed to an underground storage facility, which will hold any captured water and release slowly into the combined sewer system.

- Will the development result in a net positive or net negative change in stormwater flow? The development will result in a net decrease in stormwater volume.