City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME:

1) What was the previous permitted use for this property?

Industrial / Light Manufacturing

2) What is the proposed use for the property?

The project includes the complete demolition of the structures on the parcel. The project proposes construction of a 359 unit multi-family apartment building with studio, 1, 2, and 3 bedroom apartments spread over 5 floors above ground floor parking.

3) How is green stormwater mitigation being integrated into the proposed project?

The site was designed to minimize impervious areas to the greatest extent possible with consideration to existing and proposed uses.  The redevelopment minimizes land clearing, grading, and soil compaction.

The site is located within the City of Pittsburgh, which requires (Section §1303.04) that 20% of the existing impervious area being disturbed, when present, shall be considered meadow for modeling purposes. The green lawn space will act as permanent stabilization of the site’s undeveloped disturbed areas and will consist of grass and landscaping for all open areas.

4) Will the development result in a net positive or net negative change in stormwater flow?

The proposed stormwater management plan has been designed such that the peak runoff rate resulting from the proposed development within the studied drainage area will be equal to or less than those calculated in existing conditions for all studied design storm events as well as providing Water Quality as required by the City of Pittsburgh. Upon completion of the development, the site will result in a net negative change in stormwater flow