City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: Rosetta Street Townhomes

1) What was the previous permitted use for this property?

All existing parcels (Parcel ID Nos. 50-G-70, 50-G-69, 50-G-68, 50-G-66, 50-G-65, 50-G-63, 50-G-62, 50-G-60) are vacant residential lots.

2) What is the proposed use for the property?

The project includes the construction of five (5) duplex townhomes (10 lots total) and associated infrastructure.

3) How is green stormwater mitigation being integrated into the proposed project?

The site was designed to minimize impervious areas to the greatest extent possible with consideration to existing and proposed uses.  The redevelopment minimizes land clearing, grading, and soil compaction. The installation of proposed stormwater management facility BMPs will decrease stormwater runoff from the site.

The site is located within the City of Pittsburgh, which requires (Section §1303.04) that 20% of the existing impervious area being disturbed, when present, shall be considered meadow for modeling purposes. All water volume, quality, and rate requirements, as set forth in the City of Pittsburgh’s Stormwater Design Manual (Rev. March 2022) have been satisfied.

4) Will the development result in a net positive or net negative change in stormwater flow?

The proposed stormwater management facilities have been designed such that the peak runoff rate resulting from the proposed development within each of the studied drainage areas will be equal to or less than those calculated in existing conditions for all studied design storm events. Upon completion of the development, the site will result in a net negative change in stormwater flow.