City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME:  Carnegie Mellon University Robotics Innovation Center

1) What was the previous permitted use for this property?

Site is currently vacant.  Per the Hazelwood Green PLDP, the site is permitted for light industrial and production, research and development, office, commercial, residential (low, medium, high density), hospitality, community, and parking and transit uses.

2) What is the proposed use for the property?

Research and development

3) How is green stormwater mitigation being integrated into the proposed project?

Stormwater from the proposed area is conveyed to an area-wide infiltration pond located off-site of the proposed development.  The infiltration pond is sized to remove 1.5” (the 95% storm) via infiltration from the proposed project and surrounding contributing area.  In addition, the pond is also sized to reduce the overall rate of runoff from the Hazelwood Green development to its ultimate outfall, the Monongahela River.

4) Will the development result in a net positive or net negative change in stormwater flow?

Once the development is connected to the master infrastructure to the area-wide infiltration pond, the development will result in a net negative change in stormwater flow.