City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: Arena and Sports Performance Complex

1) What was the previous permitted use for this property?

The property is owned by University of Pittsburgh and located on their campus. The site currently consists partially of bituminous pavement, concrete pavement, and curbing all as walkways, but predominantly of meadow conditions.

2) What is the proposed use for the property?

The proposed use of the property is a new six-story arena and associated three-story sports performance complex. This will be primarily used by students, although it will offer some provisions for the public.

3) How is green stormwater mitigation being integrated into the proposed project?

Stormwater will be collected by a green roof and routed to one of two cisterns, which will work to both convey and hold stormwater volume and runoff. A chiller plant with a distribution system is currently under construction and will be operational by the time of installation of the cisterns, which would treat any captured water and reuse it throughout the campus instead of discharging to the sewers or waterways.

4) Will the development result in a net positive or net negative change in stormwater flow?

The site will experience a net decrease in stormwater volume and rate, per the city stormwater requirements, from the installation of the green roof, cisterns, and water chiller.