City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: East Liberty Site Preparation Contract – Liberty Green

1) What was the previous permitted use for this property?

The previously permitted use for this property was a vacant lot. The parcel is presently a stockpile area for excess material from surrounding construction.  The parcel had been previously planned for residential development.

2) What is the proposed use for the property?

The proposed use is to construct a public park.

3) How is green stormwater mitigation being integrated into the proposed project?

The development will meet all requirements for the City of Pittsburgh as well as the Allegheny County Conservation District.  The Urban Redevelopment Authority (URA) aims to develop responsibly.  As such, stormwater management is a vital component of the site design.  The stormwater management system consists of capturing street area and developed area, filtering it, and conveying as much as practical to the Terraced Bioswale.  In the Terraced Bioswale, the runoff volume is stored and dewaters slowly through infiltration and evapotranspiration.  Overflows and flows from large storms will discharge to the cistern and detention tank below the park facilities for additional volume management and peak rate attenuation.   Volume captured in the cistern will be re-used to irrigate the Terraced Bioswale chambers during dry periods between storm events to encourage the growth of the vegetation in those facilities.  Overflows from the cistern will be stored in the detention tanks and slowly released to the storm sewer.

4) Will the development result in a net positive or net negative change in stormwater flow?

The site will result in a net reduction/decrease in stormwater flow.  This is due to routing the stormwater runoff through the proposed stormwater management facilities as described above.  This is a net negative change in stormwater flow, but a positive change for the community.