City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: 1709-1715 Fifth Avenue

1) What was the previous permitted use for this property?

Surface parking lot.

2) What is the proposed use for the property?

The proposed property will consist of residential apartment space, tenant parking, and minimal retail space.

3) How is green stormwater mitigation being integrated into the proposed project?

The proposed stormwater management system includes inlets and underground stormwater laterals for conveyance. The total area of disturbance for the development will be less than 10,000 square feet but greater than 5,000 square feet; therefore, per Section 908.04.C of the City of Pittsburgh Code, the project must follow stormwater management regulations outlined in Chapter 1003. The project is also included in Pittsburgh’s “EcoInnovation District” and is pursuing one (1) performance point towards rainwater management. The requirements for stormwater volume retention/ removal, rate control, and water quality treatment will be met by utilizing a 3,000 sf (approximate) vegetated roof to remove approximately 720 cf of runoff.

4) Will the development result in a net positive or net negative change in stormwater flow?

After the implementation of the proposed stormwater management system, the development will result in a net nuetral change in stormwater flow.