City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: 5803 Centre Avenue Residential/Retail Development

1) What was the previous permitted use for this property?

Historically the site and structure has been used as a commercial two-story warehouse.  Currently the structure is empty and not in use.

2) What is the proposed use for the property?

The proposed use is residential and retail with a store on the first floor and 161 residential units on the remaining floors. The residences will include a mixture of 1 and 2 bedroom apartments, as well as micro and studio apartments. The building is planned to be six (6) stories.

3) How is green stormwater mitigation being integrated into the proposed project?

A StormTrap underground detention system will be added to the site, which will be internal to the building.  The underground system will store and attenuate the 2-year volume difference of stormwater runoff.  In addition, the 1-year through 100year storms will be reduced to below pre-development levels so as to improve the postdevelopment hydrology at the site. The existing warehouse site does not have any stormwater management controls. Additionally, tree pits and plantings are included in the architectural design of the building and surrounding streetscape.

4) Will the development result in a net positive or net negative change in stormwater flow?

Both the rates and volume of stormwater runoff will be reduced with the re-development of the property, due to underground detention, tree pits and plantings that are integral to the overall architectural design of the building.