City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: 27 51st Street Renovations.

1) What was the previous permitted use for this property?

The site is currently an existing 317,700 square foot warehouse that was used as a Sears Outlet Center. Currently there are no stormwater management controls for the site; all stormwater is currently entering the Allegheny County Sanitary Authority (ALCOSAN) Combined Sewer System.

2) What is the proposed use for the property?

The proposed building will remain; however, the square footage will be reduced to 258,600 square feet and is being renovated to allow for research, laboratory, warehouse and office space.

3) How is green stormwater mitigation being integrated into the proposed project?

Structural BMPs such as underground extended detention, inlets with sumps, adding impervious cover and landscape restoration are proposed at the site as an effort to improve water quality.  The stormwater is being disconnected from the existing ALCOSAN system allowing for separation of storm water and sanitary discharges.  The site prior to its current use was a rail yard, and has the potential for impacted soils thus, infiltration has not been proposed to reduce the potential for contamination to be conveyed to the Allegheny River.  Other BMP’s were evaluated for the site, but were not proposed due to the size of the site.

4) Will the development result in a net positive or net negative change in stormwater flow?

With this development, stormwater management facilities have been added to control runoff that had previously been uncontrolled and discharged directly to the ALCOSAN combined sewer system.  In addition to the stormwater facilities, ground cover changes from impervious to pervious surfaces will reduce the runoff from the site.  Due to the addition of these stormwater features, a net negative change in stormwater flow can be expected.