Amending the Pittsburgh Code, Title Nine, Zoning, all Sections by renaming the PO, Parks and Open Space district to P, Parks district; amending Section 905.02 H, Hillside district by amending lot area requirements, eliminating setback requirements, adding area of disturbance requirements; amending Article III, Section 906: Environmental Overlay Districts by adding a new overlay district as Section 906.08: SS-O, Steep Slope Overlay district and new use definitions and standards for review; and Article VI, Section 915: Environmental Performance Standards by adding new text as Chapter 915 with new definitions and standards.

Title Nine, Zoning of the Pittsburgh Code is hereby amended as follows:

A.	Change all references in the Zoning Code of PO, Parks and Open Space to P, Parks

B.	Amend Section 905.01.A - Purpose as follows:

905.01.A	Purpose

1.	Provide and maintain a system of parks for the enjoyment of the City’s residents and visitors:

2. 	[Promote public access to open space associated with specific neighborhoods] Accommodate memorial parks or cemeteries;

3.	Accommodate passive and active recreational uses [of public and private open spaces] in dedicated public and private park areas; and

4.	Protect adjacent residential neighborhoods from adverse land use impacts.

- Amend Section 905.02.C - Site Development Standards as follows:

Minimum Lot Size: 		[3200 sf]4000 sf

Minimum Front Setback:	[30 ft] none

Minimum Rear Setback:	[20 ft] none

Minimum Exterior Side Setback: [20 ft] none

Minimum Interior Side Setback: [5 ft] none

D.	Add the following to Section 905.02.C - Site Development Standards:

Maximum Area of Disturbance: 30% of total lot area or 1800 sf, whichever is less

E.	Add the following to 905.02.D - Special Definitions:

3.	Area of disturbance: area of the site where vegetation is removed, structures or paving are built, or excavation occurs.

F.	Delete all of Section 905.02.E - Hillside Development Guidelines as follows:

[905.02.E Hillside Development Guidelines

905.02.E.1 Purpose and Intent

It is the purpose of the Hillside District to ensure that development occurs in such a manner as to protect the natural and topographic character and identity of these areas, environmental resources, the aesthetic qualities and restorative value of lands, and the public health, safety, and general welfare by insuring that development does not create soil erosion, silting of lower slopes, slide damage, flooding problems, and severe cutting or scarring. It is the intent of this zone to encourage a sensitive form of development and to allow for a reasonable and responsible development that complements the natural and visual character of the City. Reference is made to hillside development guidelines when making the required findings of fact.

905.02.E.2 Applied

Every new or changed use of land and every structure hereafter erected or enlarged in the H District shall comply with the following guidelines:

905.02.E.3 Findings of Fact

In reviewing an application for a Permit, the Zoning Administrator shall make the following findings of fact in the review process:

a.     The site is physically suitable for the design and siting of the proposed 	development. The proposed development will result in minimum disturbance 	of sensitive areas.

b.     The grading and excavation proposed in connection with the development will 	not result in soil erosion, silting of lower slopes, slide damage, flooding, 	severe scarring, or any other geological instability that would affect health, 	safety, and general welfare as determined by the Zoning Administrator. 	Disturbed slopes are planted with native and self-sufficient vegetation.

c.     The proposed development retains the visual quality of the site, the aesthetic 	qualities of the area, and the neighborhood characteristics by utilizing proper 	structural scale and character, varied architectural treatments, and 	appropriate plant material.

905.02.E.4 Guidelines

FINDING: The site is physically suitable for the design and siting of the proposed development. The proposed development will result in minimum disturbance 	of sensitive areas.

Guideline 1: Design structures to fit into the hillside rather than altering the hillside to fit the structure.

a.     	Standard prepared pads resulting in grading outside of the building footprint 	and driveway area shall be discouraged.

b.     	Use retaining structures as an alternative to banks of cut-and-fill. Design and 	site such structures to avoid adverse visual impact.

c.     	Consider "unconventional structures" that will fit into the hillside. This would 	include: (1) stilt houses; (2) reduced footprint design; (3) multiple "step-up" 	or "step-down" structures; or (4) structures with open foundations, if 	landscaping screens the underside area of the building.

d.     	Use a foundation type that is compatible with existing hillside conditions.

Guideline 2: Development shall be sited on the least sensitive portion of the site to preserve the natural landforms, geological features, and vegetation.

a.     	Design and locate structures so they fit into the contour of the hillside and 	relate to the form of the terrain.

b.     	Locate development to minimize disturbance of the sensitive area.

c.    	Minimize coverage by using multilevel structures.

d.     	Cluster development away from open space valleys as close to existing 	development as possible.

e.     	Avoid disturbance of major rock outcroppings, major trees, waterways, ridge 	lines, natural plant formations, and known archaeological sites.

f.     	Major structures must be sited so that only a portion can be seen beyond 	the hill's brow or profile, when viewed from major public roadways or viewing 	places.

g.     	When appropriate, place structure as close to the street as possible to 	preserve the natural terrain. In some cases this would require development 	on the steep portions to preserve the valleys or development on the flat 	portions to preserve the hillsides.

Guideline 3: Development should not occur directly on the brow of the hill, since disturbing this portion of the hill will often cause erosion below the disturbed area.

a.     	Where level land above the brow, or hillside land below the brow, is not 	available within the lot, the brow may be developed, subject to site plan 	review, if particular caution is taken to prevent erosion beneath the 	developed area.

b.     	The design of a structure on a brow should be small in scale and should be 	particularly sensitive to the contours of the land.

FINDING: The grading and excavation proposed in connection with the development will not result in soil erosion, silting of lower slopes, slide damage, flooding, severe scarring, or any other geological instability that would affect health, safety, and general welfare, as determined by the Zoning Administrator. Disturbed slopes are planted with native and self-sufficient vegetation.

Guideline 4: Limit the amount of impervious surfaces. Design and site such surfaces to support the natural system of drainage.

a.     	Design drainage systems away from neighboring properties and into the 	existing water-flow pattern.

b.     	Use wooden decks instead of concrete slabs for patios.

c.     	Pervious materials shall be used for parking (including, but not limited to, 	structural soil, partial paving, and gravel). Impervious material shall be 	permitted at the discretion of the Zoning Administrator.

d.     	Reduce width of street improvements, reduce sidewalk requirements, use 	common driveways and cluster units, if open space will thereby be 	preserved.

Guideline 5: The site should be replanted with self-sufficient trees, shrubs, and ground cover that are compatible with existing surrounding vegetation.

a.     	All manufactured slopes shall be planted with erosion control and self-	sufficient plantings.

b.     	Transitional slopes should be planted to enhance the blending between 	manufactured and natural slopes.

c.     	Landscaping plans should not require excessive irrigation.

d.     	Vegetation shall overlap the structure, especially at the foundation. Invasive 	plantings, as identified by the prohibited planting list maintained by the 	Zoning Administrator, are prohibited.

Guideline 6: Utilize the structural quality of the soil as a determinant of the type of construction.

a.     	Assure hillside stability both during and after construction by recognizing soil 	characteristics, hydrology, and the slope of the terrain.

b.     	Existing vegetation shall not be needlessly displaced, degraded, or 	destroyed. In no case shall more than ten (10) percent of the lot, or two 	thousand four hundred (2,400) square feet, whichever is larger, be cleared.

c.     	The soil, within the drip line of trees that are to remain, shall be protected. 	All excavation or earth modifications are to be planted.

Guideline 7: In cases where cut-and-fill grading are required, the slopes shall avoid straight and unnatural slope faces.

a.     	All manufactured slopes shall be planted with erosion control and self-	sufficient plantings.

b.     	Transitional slopes should be planted to enhance the blending between 	manufactured and natural slopes.

c.     	Land down slope must be protected from falling debris and abnormal site 	drainage.

FINDING: The proposed development retains the visual quality of the site, the aesthetic qualities of the area, and the neighborhood characteristics by utilizing proper structural scale and character, varied architectural treatments, and appropriate plant material.

Guideline 8: Employ a variation in architectural design.

a.     	Design the garage space to be either under or beside the structure 	depending on whether the lot is uphill or downhill from the street.

b.     	Automobile storage shall be screened according to Section 918, and shall 	not disrupt slopes.

c.     	Parking areas shall respect natural contour lines.

d.     	Use deck areas, either on the roof of the garage, or the house, or extending 	from the house to reduce the amount of grading.

e.     	Views of the deck shall not be a visual intrusion on the hillside. Supporting 	structures shall be screened from view with appropriate vegetation.

f.     	Employ zero lot line developments, at the discretion of the Zoning 	Administrator, where permitted by zoning if visual or open space qualities 	can be gained.

g.     	Vary the treatment of rooftops to avoid the monotony of materials, forms, 	and colors. Rooftop utilities and mechanical equipment should be avoided.

h.     	Mechanical equipment and trash receptacles shall be screened to the extent 	that they are not visible.

Guideline 9: Consider existing vegetation when landscaping the site.

a.     	Protect existing resources from being trampled or destroyed.

b.     	Keep new landscaping compatible with existing vegetation and the scenic 	character of the area.

c.     	Preserve the natural landscaping on slopes adjacent to natural sloping 	areas.

Guideline 10: Match scale and character of buildings with scale and character of terrain and the surrounding neighborhood.

a.     	Keep the scale (height and bulk) of the structure compatible with the site 	and the neighborhood.

b.     	Do not create development patterns that form visually protruding horizontal 	bands or vertical bulk. A mixture of shapes, subordinate and compatible with 	the site and area, should be achieved.

c.     	Irregular architectural edges should be used to interlock structures with 	hillside contours and vegetation.

d.     	Avoid visible construction cuts and permanent scarring.

Guideline 11: Structures shall be sited not only to provide views from the structure but also to provide a variety of community and private viewing places.

a.     	Community or public land use should be made of those portions of hillsides 	most exposed to public view or from which the widest views are possible.

b.     	Views from public places (roadways, walks, observation points, parks, or 	greenways) shall be maintained.

c.     	When viewed from below, all supporting structures, girders, piers, etc. must 	be screened.

905.02.F Applicability

Any one (1) of the following factors will be considered when determining whether an H District should be applied to a geographic area in the City of Pittsburgh.

1.     	Areas that were formally zoned "S".

2.     	Areas that have a contiguous land area of at least one (1) acre in size that is 	comprised of an area that has an average slope in excess of twenty-five (25) 	percent.

3.     	Areas that are mapped by the City of Pittsburgh as Landslide-Prone Areas. ]

(Ord. 35-2002, §§ 1A, AB, eff. 12-3-02)

- Add Section 905.02.C - Site Development Standards as follows:

906.08	SS-O, Steep Slope Overlay District

906.08.A	Purpose

1.	Establish the attributes and limitations of Pittsburgh’s steep slope areas.

2.	Assure that the steep slope site is appropriate for development considering natural site limitations, associated hazards, public safety, and the need to provide public services and infrastructure.

3.	Assure that the design of the proposed development responds to the site’s limitations and attributes.

4.	Recognize the importance of the city’s steep slopes in defining the character of Pittsburgh.

906.08.B	Special Definitions

1. 	Slope: inclination of land expressed as a percentage and derived by dividing the vertical elevation change by the horizontal distance.

2. 	Brow of slope: that portion of a hillside that forms the horizon when viewed from below and afar; that area where the steep slope interfaces with less steeply sloped land above and beyond the SS-O, Steep Slope Overlay boundary.

3. 	Foot of slope: transitional point between the valley floor and the hillside; area where the steep slope interfaces with less steeply sloped land below and beyond the SS-O, Steep Slope Overlay boundary.

4. 	High Visibility Area: area defined and mapped by An Ecological and Physical Investigation of Pittsburgh Hillsides as city hillside areas that are visible by a large number of people on a daily basis due to the ability of the slope to be viewed from long distances, many vantage points, or numerous significant public viewing areas.

5.	Transition Area: buffer area located adjacent to the top and bottom of the steep slope area (brow or toe of the steep slope area) where both the land and the associated land use regulations change form; 100 foot area setback from the boundary of the SS-O, Steep Slope Overlay.

6.	Native Vegetation: species of plants that exist in this area prior to European settlement; plants within their pre European settlement range or zone of potential dispersal.

7.	Invasives: plants which aggressively spread and displace beneficial vegetation.

8.	Disturbed area: area of the site where vegetation is removed, structures or paving is removed, or excavation occurs.

906.08.C	Use Regulations

To ensure that development occurs in a manner to protect the natural and topographic character of steep hillsides and to encourage sensitive development that complements the natural and visual character of the City’s hillsides, land may be used and structures may be erected, altered or enlarged for uses allowed in the underlying zoning district as further regulated by the provisions of this section.

906.08.C.1	Slopes between 25% and 40%

All uses in the SS-O district on slopes between 25% and 40% shall be permitted as a Special Exception in accordance with the procedures of Section 922.07 and subject to the review criteria of Section 906.08.D.

906.08.C.1	Slopes in excess of 40%

All uses in the SS-O district on slopes in excess of 40% shall be permitted as a Conditional Use in accordance with the procedures of Section 922.06 and subject to the review criteria of Section 906.08.D.

906.08.D	Review Standards

The following standards shall apply within the SS-O, Steep Slope Overlay district.

1.	The proposed structure shall be designed to fit into the hillside rather than altering the hillside to fit the structure and may include the following;

(a)	retaining structures instead of banks of cut-and-fill;

(b)	structures that fit into the hillside including stilt houses, reduced footprint design, multiple "step-up" or "step-down" structures and structures with open foundations with landscaping screening  the underside of the building;

(c)	foundation types that are compatible with existing hillside conditions.

2.	The development shall be sited on the least sensitive portion of the site to preserve the natural landforms, geological features, major rock outcroppings, major trees, waterways, ridge lines, natural plant formations, and known archaeological sites and shall follow the contour of the hillside and relate to the form of the terrain;

3. 	Development shall not occur directly on the brow of the hill to prevent erosion below the disturbed area unless the design of the structure on a brow is small in scale;

4. 	The development shall limit the amount of impervious surfaces by including pervious materials (including, but not limited to, structural soil, partial paving, and gravel) and shall support the natural system of drainage;

5.	The site shall be replanted with self-sufficient, compatible native vegetation that does not require excessive irrigation;

6.	The development shall utilize the structural quality of the soil as a determinant of the type of construction;

7.	In cases where cut-and-fill grading are required, the slopes shall avoid straight and unnatural slope faces.  All manufactured slopes shall be planted with erosion control and self-sufficient plantings and transitional slopes shall be planted to enhance the blending between manufactured and natural slopes;

8.	The development shall employ a variation in architectural design and shall include a variety of rooftops, materials, forms, and colors. Rooftop utilities and mechanical equipment should be avoided;

9.	The development shall consider existing vegetation when landscaping the site;

10.	Structures shall be of a scale and character that is contextual with the scale and character of terrain and the surrounding neighborhood. All supporting structures, girders, piers, etc. must be screened; and

11.	Structures shall be sited not only to provide views from the structure but also to provide a variety of community and private viewing places.

- Insert into Chapter 915 as follows:

CHAPTER 915: ENVIRONMENTAL PERFORMANCE STANDARDS

915.01	General

915.02	Environmental Standards

915.03	Hillside Compatibility Standards

915.01	General

915.01.A	Purpose

The City’s natural resources, steep forested hills, prominent ridges and rivers are major contributors to the quality of life and distinctive character.  The provisions of this section are intended to protect sensitive environmental areas from adverse impacts.

915.01.B	Applicability

No structure or land use shall be located, erected, constructed, reconstructed, moved, altered, converted, enlarged or designed to be so, except in conformance the provisions of this section.

915.02	Environmental Standards

915.02.A	Grading Standards

915.02.A.1	The grading, cut, and fill standards of this section shall apply to all slopes.

a.	To the maximum extent feasible, the grading shall preserve the natural landforms of the site;

b.	To the maximum extent feasible, cutting, filling and severe benching or terracing of existing slopes to create additional building area or larger building sites shall be avoided;

c.	Finished grades of 15% or less are strongly encouraged. Cut or filled slopes shall not exceed 25% unless:

(1)	The applicant submits a geotechnical investigation report that certifies the safety and suitability of such slopes; and

(2)	The applicant proposes the use of walls, terraces, or other methods at intervals of not less than ten (10) feet to create planting beds that will stabilize the slope, and such measures are approved in the geotechnical investigation report as sufficient to ensure the stability of the slope and ensure that such slope shall pose no significant risk of danger to any property or public improvements located on or off the proposed development site.

d.	The top and bottom of the cut or filled slopes shall be located:

(1)	No less than ten (10) feet from any street, building, parking area, or other developed area; and

(2)	No less than five (5) feet from any adjacent property line.

e.	Retaining walls or gabions may be permitted to support steep slopes, but shall not exceed ten (10) feet in height.

915.02.B	Slope Revegatation Standards

Slopes in excess of a fifteen (15) percent grade that are exposed during construction or site development shall be landscaped or revegetated in order to mitigate adverse environmental and visual effects. Fill soil on slopes must support plant growth. At a minimum, any slope in excess of fifteen (15) percent grade exposed or created during development shall be landscaped or revegetated with trees and other plant material at the following minimum planting densities per one hundred fifty (150) square feet of exposed slope area:

• One (1) canopy tree 			• two (2) understory trees

• Two (2) evergreens 			• five (5) shrubs

• Gabions and low walls should be utilized to gain planting pockets on steep grades.

915.02.C	Tree and Vegetative Surveys

The Zoning Administrator may require a tree survey for development applications for any site greater than one (1) acre.

915.02.D	Tree Protection and Replacement

The Zoning Administrator may require the protection and preservation of trees with a diameter of twenty-four (24) inches or more, measured at a point four (4) feet above grade. If said trees, required of the Zoning Administrator to be protected and preserved, are removed during site preparation or development, they shall be replaced. The combined total diameter of replaced trees shall be, at a minimum, equal to the combined total diameter of removed trees. Diameter measurements shall be taken at a point four (4) feet above grade.

915.03	Hillside Compatibility Standards

915.03.A 	Purpose

The Hillside Compatibility Standards are intended to protect the City’s hillsides from the adverse impacts sometimes associated with development.

915.03.B	Applicability

The regulations of the Hillside Compatibility Standards shall apply to all zoning districts when development is located:

(a)	In the H, Hillside district;

(b)	Within one hundred (100) feet of property in the SS-O, Steep Slope Overlay 	district.

915.03.C 	Site Plan Review

All development that is subject to Hillside Compatibility Standards shall require site plan review and approval in accordance with the Site Plan Review procedures of Sec. 922.04.

915.03.D	Height

1.	Within 100 Feet of Brow or Foot of the Slope

Structures or portions of structures shall not exceed twenty-five (25) feet or two (2) stories in height when located within one hundred (100) feet of the Brow or Toe of the Slope

2.	More Than 100 Feet from Brow or Foot of the Slope

No compatibility-related height restrictions shall be imposed on structures located more than one hundred (100) feet from the Brow or Toe of the Slope.

915.03.E 	Setback

All development shall be setback at least fifty (50) from the Brow of the Slope.

915.03.F	Site Design

The following additional site design standards shall apply to development that is subject to the Hillside Compatibility Standards of this Chapter.

1.	New development shall be located to maintain views to and from the Brow of the slope; and

2.	All on-site lighting shall be shielded to prevent light spillover onto adjacent properties.

915.03.G	Waiver of Residential Compatibility Standards

The Zoning Board of Adjustment may approve a Special Exception according to the provisions of Sec. 922.07 to waive the Hillside Compatibility Standards imposed by this Chapter, subject to the following standards:

1.	The Board shall determine that the waiver will not create detrimental impacts on the surrounding properties, taking into consideration the physical relationship of the proposed use and structure to surrounding uses and structures;

2.	The Board shall impose alternative methods which will cause the development to comply with the purpose of the Hillside Compatibility Standards;

3.	Building height restrictions found in this chapter may be waived only if there is a taller intervening structure between the proposed structure and the adjacent residential zoning district, in which case the height shall be limited to the height of the intervening structure.

I.	Delete all of Section 922.04.E.5 - Environmental Impact Mitigation as follows:

[5. 	For all properties or uses specifically required by the Code to undergo site plan review, the following Environmental Impact Mitigation standards shall apply:

a.	The grading, cut, and fill standards of this section shall apply to all slopes in 	excess of fifteen (15) percent.

i.	To the maximum extent feasible, the applicant shall preserve the natural landforms of the site.

ii.	To the maximum extent feasible, cutting, filling and severe benching or terracing of existing slopes to create additional building area or larger building sites shall be avoided.

iii.	Finished grades of twenty-five (25) percent or less are strongly encouraged. Cut or filled slopes shall not exceed forty (40) percent grade unless:

(a)	The applicant submits a geotechnical investigation report that certifies the safety and suitability of such slopes; and

(b) 	The applicant proposes the use of walls, terraces, or other methods at intervals of not less than ten (10) feet to create planting beds that will stabilize the slope, and such measures are approved in the geotechnical investigation report as sufficient to ensure the stability of the slope and ensure that such slope shall pose no significant risk of danger to any property or public improvements located on or off the proposed development site.

iv. 	The top and bottom of the cut or filled slopes shall be located:

(a)	No less than ten (10) feet from any street, building, parking area, or other developed area; and

(b) 	No less than five (5) feet from any adjacent property line.

v. 	Retaining walls or gabions may be permitted to support steep slopes, but shall not exceed five (5) feet in height.

b. 	Slopes in excess of a fifteen (15) percent grade that are exposed during construction or site development shall be landscaped or revegetated in order to mitigate adverse environmental and visual effects. Fill soil on slopes must support plant growth. At a minimum, any slope in excess of fifteen (15) percent grade exposed or created during development shall be landscaped or revegetated with trees and other plant material at the following minimum planting densities per one hundred fifty (150) square feet of exposed slope area:

• One (1) canopy tree 			• two (2) understory trees

• Two (2) evergreens 			• five (5) shrubs

Gabions and low walls should be utilized to gain planting pockets on steep 	grades.

c.  	Tree and Vegetative Surveys

The Zoning Administrator may require a tree survey for development applications for any site greater than one (1) acre.

d.  	Tree Protection and Replacement

The Zoning Administrator may require the protection and preservation of trees with a diameter of twenty-four (24) inches or more, measured at a point four (4) feet above grade. If said trees, required of the Zoning Administrator to be protected and preserved, are removed during site preparation or development, they shall be replaced. The combined total diameter of replaced trees shall be, at a minimum, equal to the combined total diameter of removed trees. Diameter measurements shall be taken at a point four (4) feet above grade.]