City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: Harvard Beatty Housing

1) What was the previous permitted use for this property?

Parking Lot

2) What is the proposed use for the property?

Residential Building

3) How is green stormwater mitigation being integrated into the proposed project?

This Stormwater Management (SWM) Plan was developed in support of the Harvard Beatty Housing, LLC development project. As the project area involves regulated activities that result in cumulative earth disturbances equal to or greater than ten thousand (10,000) square feet but less than one (1) acre, the Simplified Method (consistent with CG-2 in the PADEP Pennsylvania Stormwater BMP Manual) was applied to establish the level of required stormwater controls.

A subsurface infiltration bed BMP was designed below the proposed parking lot to manage collected runoff from the drainage system collection features such as roof drain downspouts and inlets/catch basins. To meet the requirements of Section 1303.03 – Volume Controls, the infiltration bed was sized to capture the first two (2) inches of runoff from impervious surfaces with a permanent retention of 1.65 inches. This BMP disperses collected runoff across the R-Tank chambers area and aggregate bedding to promote infiltration. A low-flow orifice dewaters the BMP over a 72-hour period following the storm event, ultimately discharging to an outlet structure with connection to the adjacent combined sewer

4) Will the development result in a net positive or net negative change in stormwater flow?

The project will result in a reduction in stormwater runoff as a result of the proposed increase in landscaped area within the private parcel coupled with the addition of tree boxes/street trees within the street right-of-way.