City of Pittsburgh

Sewer Facilities Planning Module Questionnaire

PROJECT NAME: 2400 E. Carson Street

1) What was the previous permitted use for this property?

Parcel 12-L-236-0-2 previous permitted use for the property is Charitable exemption/ hos/homes and Parcel 12-L-264 previous permitted use for the property is vacant commercial land.

2) What is the proposed use for the property?

The project includes the renovation of the structures located at 2400 E. Carson Street and the

construction of a parking lot/playground area located to the south to serve the building. The

project proposes renovations to the existing structure to include space for a community daycare center and therapy program for children ages 5 and under that experience some behavioral and emotional disruptions.

3) How is green stormwater mitigation being integrated into the proposed project?

The site was designed to minimize impervious areas to the greatest extent possible with consideration to existing and proposed uses.  The redevelopment minimizes land clearing, grading, and soil compaction. The installation of proposed storm water management facility BMPs will enhance the runoff from the site.

The site is located within the City of Pittsburgh, which requires (Section §1303.04) that 20% of the existing impervious area being disturbed, when present, shall be considered meadow for modeling purposes. This project does not propose disturbance of existing impervious areas.  In addition, the increase in runoff volume from the 2-year storm event shall be removed or captured, filtered and/or released via extended detention, while also providing rate control for the 1-, 2-, 10, 25-, 50-, and 100-year frequency storm events.

4) Will the development result in a net positive or net negative change in stormwater flow?

The proposed stormwater management facilities have been designed such that the peak runoff rate resulting from the proposed development within each of the studied drainage areas will be equal to or less than those calculated in existing conditions for all studied design storm events as well as providing Water Quality as required by the City of Pittsburgh. Upon completion of the development, the site will result in a net negative change in stormwater flow.